## Slide 1: Build your own gas turbine performance model in Python
Tutorial of Basics
ASME IGTI TE 2025 Aircraft Engine Committee
Dr. Wilfried Visser
Oscar Kogenhop MSc

## Slide 2: Overview
Introduction
System performance modelling
  Propulsion and power systems
Software implementation
Case study: jet engine python model
Concluding remarks

## Slide 3: For whom is this tutorial
Engineers, scientists, researchers, students
  With interest in system simulation of propulsion and power systems
  Wanting to learn how system models work
  Needing for models with new functionalities
    Coupling with other models
  Having basic coding skills
Introduction

## Slide 4: Key focus areas
System model basic elements
Object orientation
Python programming language
  Open-source libraries
    Aero-thermal
    Numerical methods
    Data handling
    Visualization
Introduction

## Slide 5: System performance modeling
System of interacting components
  Relationships among system of interacting components
  Component models
Equations
  conservation of mass, energy, momentum, other…
  mostly non-linear algebraic/differential
Component operating points
  Defined by state variables
Solution of set of equations
  State variable vector representing valid system operating point
  Steady-state or transient

## Slide 6: Propulsion and power systems
Gas turbines
  Aero engines: jet engines, turboprop, turboshaft
  Land based engines: turboshaft
Propellers and rotors
Hybrid elements
  Electric motors
  Generators
  Fuel cells
  Batteries
Alternative/sustainable fuels
System performance modeling

## Slide 7: Propulsion and power system performance prediction
Design studies
Existing designs
System performance modeling

## Slide 8: Gas turbine system performance models
Components models
  intake, fans/compressors, combustors, turbines, mixers, exhausts,
  Component maps
State variables
  Rotor speeds, mass flows, pressure ratios, …
Equations
  Mass flow in = mass flow out (at component intersections, engine stations)
  Power balance : PWcompressor = PWturbine
Input
  Fuel flow, TIT, inlet P and T…
Output
  Thrust FN, Power, Fuel flow, Efficiency, P, T at engine stations…
System performance modeling

## Slide 9: New propulsion system model elements
Sustainable fuels
Electric systems
Heat exchangers
Hybrid systems (gas turbines, fuel cells, batteries)
Generators, Electric motors driving fans and propellers
So, there is a need for
  Extensions in modeling and simulation tools
  Or, build tools from scratch ?
System performance modeling

## Slide 10: From scratch ?
Things to think about
  Why from scratch?
  Will others use my code?
  Will code be used later?
    For other propulsion systems / engines?
    Flexibility
  Costs / Benefits of making the tool generic?
    Add a user-friendly GUI?
  ?...
Save time and $ preparing your project
  Select language, development platform
  Design software architecture
System performance modeling

## Slide 11: Why from scratch?
Pros
  Full control and flexibility
  “I know what I am doing”
  Coupling with other models (1..4 D models)
Cons
  A lot of work
    Validation
    Code maintenance / documentation
  Code accessibility / readability to others
    Especially ‘if you leave the company’
System performance modeling

## Slide 12: Software implementation
So, you have decided to start
from scratch!

## Slide 13: Language / development environment
Python
  Open-source programming language/development environment
  Widely used by students, young engineers and scientists
  Ready to use libraries for almost any engineering problem
  Object orientation
  Readable code
Development environments
  Microsoft Visual Studio Code (‘VS Code’)
  PyCharm
Platform? Windows, Linux, IOS?
Software implementation

## Slide 14: Python implementation
Run code from development environment (no GUI)
Specify input in code
  Example: specify Ambient conditions and a number of fuel flow steps
Adapt code where needed
Software implementation

## Slide 15: Python open-source libraries
Ready to use libraries
  Standard atmosphere aero-calc
  Thermodynamics cantera
    Compression, expansion in compressors, turbine, exhausts, nozzles
    Combustion chemical reactor model
  Numerical methods scipy
    ‘root’ generic solver (‘Krylov’ method)
  Output data export
    Export to .csv pandas
    Make graphs in Excel
Software implementation

## Slide 16: Aero-calc library
Aero-calc functions used for calculation of ambient/flight conditions from altitude, flight Mach, dT
  alt2temp
  alt2press
  temp2speed_of_sound
Software implementation

## Slide 17: Cantera library
Open-source suite of tools for problems involving chemical kinetics, thermodynamics, and transport processes
https://cantera.org/index.html
Jetsurf machanism used for
  Gas path transport
  Compression/expansion
  Combustion
Software implementation
https://web.stanford.edu/group/haiwanglab/JetSurF/JetSurF2.0/Index.html

## Slide 18: Using Cantera (ct) gas model
  define gas model
    gas = ct.Solution('jetsurf.yaml’)
  Set T, P, composition (mass mixing ratios)
    gas.TPY = 1200, 101325, 'CH4:1, O2:2, N2:7.52’
  Get T or P
    P = gas.P
    T = gas.T
Software implementation

## Slide 19: Using Cantera (ct) mass flow/transport
  Define a quantity (mass flow) of gas
    GasIn = ct.Quantity(gas, mass flow)
  Set mass flow entropy or enthalpy and pressure
    GasIn.SP = entropy value, pressure value
    GasIn.HP = enthalpy value, pressure value
  Isentropic compression of GasIn mass flow (with pressure ratio PR)
Software implementation

## Slide 20: Using Cantera (ct) combustion
  2 options for fuel specification
    User specified composition (single species)
    T and P
  or
    User specified LHV (mix of ‘unknown’ species, e.g. Kerosine, Jet-A)
    T and P
    average H/C and O/C ratio of the fuel molecules
  In both cases end H, T, P and composition can be calculated
Software implementation

## Slide 21: User specified fuel composition
    fuel = ct.Quantity(fg.gas) define fuel
    fuel.mass = fuel mass flow fuel.TPY = T, P, FuelComposition define T, P, composition
    GasOut = GasIn + fuel mix fuel with air
    GasOut.equilibrate('HP’) chemical equilibrium combustion end state
    T4 = GasOut.T get combustion end T (or H, S etc)
Cantera - combustion

## Slide 22: User specified LHV
  More complicated
  Cannot use Equilibrate function
  Need to calculate end composition from
    Air composition
    Fuel H/C and O/C ratios
    Mole fractions book keeping (converting between mass – moles)
Cantera - combustion

## Slide 23: User specified LHV code
    Little bit more code lines:
Cantera - combustion

## Slide 24: Python implementation - output
Generate global output table pandas
  Code output per component
  System level output (PW, FN, Wf, W2 etc.)
  Export to .csv
  Make graphs in Excel
Component maps
  Graphical output matplotlib
  Compessors, fans, turbines, …
  Draw operating lines in maps
    scaling
Software implementation

## Slide 25: Object orientation
3 main paradigms
  Encapsulation
    An object holds both data and ‘methods’ (procedures, functions) working with these and data, and also external data
    Object class (class is ‘type’ of object)
  Inheritance
    An object can inherit data and methods from a ‘parent class’
  Polymorphism
    An object variable can represent objects from different classes inheriting from the same parent
Software implementation

## Slide 26: Encapsulation example
Compressor component model
  compressor object class holds
    W, PR, Eta, N
    methods to calculate the compression process
    Compressor performance map
    Functions to communicate with the system model and other component models
Software implementation

## Slide 27: Inheritance example
Gas path W, T, P in/out
Inlet
Turbomachinery N, PR, Eta, PW
Controls
Fuel control
Duct
Combustor fuel flow
….
Compressor compression
Turbine expansion
Fan splitter
….
Exhaust PR, thrust
instantiable class
abstract class
Generic component model class
data
functions, procedures (algorithms)
Software implementation
legend

## Slide 28: Polymorphism example
Generic component model class object
  ‘abstract’ object that can represent any child object
  has a generic ‘Run’ method (procedure or function)
  Child classes inherit and ‘override’ the Run procedure with calculations actually simulating the process in the component
System model
  List of objects (of instantiable classes)
    E.g. Inlet-compressor-combustor-turbine-exhaust
    System model simulation subsequently calls the ‘Run’ methods of all objects in the list, in this example calculating from inlet through exhaust….
Abstract Generic component model class
  Encapsulation
    An object holds both data and ‘methods’ (procedures, functions) working with these and data, and also external data
    Object class (class is ‘type’ of object)
  Inheritance
    An object can inherit data and methods from a ‘parent class’
  Polymorphism
    An object variable can represent objects from different classes inheriting from the same parent
Software implementation

## Slide 29: Polymorphism python code example
# create a turbojet model list of component models
turbojet = [TInlet( 'Inlet1', 19.9, 1 ),
TCompressor('compressor1', 1, 16540, 6.92, 0.825),
TCombustor( 'combustor1', 0.38, 0, 1, 1 ),
TTurbine( 'turbine1', 1, 16540, 0.88 ),
TDuct( 'exhaustduct', 1 ),
TExhaust( 'exhaust1', 1, 1, 1 )]
……
# comp is the abstract component object
for comp in turbojet:
q_gas = comp.Run(Mode, q_gas, Ambient)
Software implementation
Class
Name
Design/object data

## Slide 30: Adapting the baseline code
Other engine configurations
  Turbofan
  Mixer
  Recuperator / heat exchanger
  Turbogenerator
Add propulsion system elements
  Generators, electric motors, propulsors, batteries, fuel cells
Software implementation

## Slide 31: Adapting the baseline code
Component model extensions
  Variable geometry
  Bleed
  Turbine cooling
  1-D model code
  Other fuels
    Easily adapt fuel in combustor component (cantera)
  …
Software implementation

## Slide 32: Adapting the baseline code
API (Application Programming Interface)
  Couple with other models
Extend user interface
  Extend output
    Graphs, tables, export
  Add GUI
Software implementation

## Slide 33: Main program code
# Generic gas turbine components
inlet1 = TInlet('Inlet1', '', 0,2, 19.9, 1 )
duct1 = TDuct('exhduct', '', 5,7, 1.0 )
exhaust1 = TExhaust('exhaust1', '', 7,8,9, 1, 1, 1, 1 )
# ***************** Combustor ******************************************************
# fuel input
combustor1 = TCombustor('combustor1', '', 3, 4, 0.38, None, 1, 1, None, 43031, 1.9167, 0, '')
compressor1 = TCompressor('compressor1','compmap.map' , 2, 3, 1, 16540, 0.825, 1, 0.75 , 6.92, 'GG')
turbine1 = TTurbine( 'turbine1' ,'turbimap.map', 4, 5, 1, 16540, 0.88 , 1, 0.50943, 0.99, 'GG’)
fsys.systemmodel = [inlet1,
compressor1,
combustor1,
turbine1,
duct1,
exhaust1]
Software implementation

## Slide 34: Relationships among component models
Ambient
  Inlet, exhausts
Gas path
  Gas conditions and flow rates between two connected components
  Engine station numbering
  Example: compressor – combustor, station nr. 3
Shafts
  Power balance PWcompressor = PWturbine
  If no balance: transient (accel or decel)
Heat transfer
Control
  Fuel flow, variable geometry
Software implementation

## Slide 35: Passing gas conditions in Python
# use dictionary for gas path conditions oriented by gas path station number
gaspath_conditions = {}
def Run(self, Mode, PointTime):
…
self.GasIn = fsys.gaspath_conditions[self.stationin]
…
# Calculate self.GasOut
…
fsys.gaspath_conditions[self.stationout] = self.GasOut
return self.GasOut
Software implementation

## Slide 36: Extending the models - 1
Fidelity
  1-D component models
    Turbomachinery
    Combustors
  Couple with multi-D CFD models
Gas turbine system
  Control system
  Fans, mixers
  Recuperators
Software implementation

## Slide 37: Extending the models - 2
Propulsion system elements
  Loads (propellers, generators)
  Hybrid propulsion systems
    Batteries
    Fuel cells
Software implementation

## Slide 38: Conclusion

## Slide 39: Questions?

## Slide 40: Aero engine inlet ram compression
Jet engine inlet example
internal diffusion (compression)
external diffusion (compression)
“inlet efficiency”
0
1
2

## Slide 41: T-S diagram, turbojet REAL cycle
T
S
0
2
3
c02
2cp
C0 = air speed
C8 = propelling jet velocity
4
5
8
turbine
nozzle
c82
2cp
1
pressure loss
station 1 = inlet front
1-2 : inlet losses
p0

## Slide 42: T-S diagram, afterburning turbojet (reheat)
T
S
c02
2cp
C0 = air speed
C8 = propelling jet velocity
0
2
3
4
5
8 (9 with con-di nozzle)
turbine
nozzle
c82
2cp
1
pressure loss
p0
afterburner

## Slide 43: T-S diagram, turbofan REAL cycle
T
S
0
2
3
c02
2cp
unmixed turbofan
C0 = air speed
C8 = propelling jet velocity
4
5
8
HP turbine
hot nozzle expansion
c82
2cp
1
pressure loss
cold nozzle expansion
25
p0
45
LP turbine

## Slide 44: Dimensionless groups
Turbomachinery
  Compressors, Fans, Turbines
  (propellers, helicopter rotors)
Performance representation (ideal gas)
  ‘Function’ of D, N, m, P01, P02, T01, T02, ν (or μ), γ (cp/cv)
  Dimensional analysis (Pi theorem):
    3 fundamental units present (M, T, L)
    Number of variables reducible by 3 into 9-3 = 6 non-dim. groups
    Relations among which describe performance
  4 primary groups
  2 groups often ignored for gas turbines
    effect viscosity ν or μ (Re) marginal on efficiency, ‘only’ high altitude
    Gamma γ only if using different media (e.g. process industry, organic rankine, scCO2 cycles) or large temperature changes (γ = F(T))
D
m
N
γ, μ
P02, T02
P01, T01

## Slide 45: Dimensionless groups - Reynolds
Effect of kinematic viscosity ν represented by Reynolds number
For axial turbomachinery:
  (L = blade chord length, V is blade relative velocity, ν = kinematic viscosity)
Effect of Re is small
  Primarily on efficiency
    Small corrections as function of Re change
  Aero engines
    at high altitudes / low ambient temperatures
    higher ν (= μ/ρ)

## Slide 46: Compressor characteristics
Equilibrium running line
h
p
m
θ
N
θ
A
0,2
p
0,3
comp
Surge line
curves of constant
δ

## Slide 47: Turbine characteristics
N
θ
N
θ
PR =p
/
p
h
m
θ
δ
choking
turb
0,4
0,5

## Slide 48: Inlet characteristics
Pressure loss function
  ‘Ram recovery’ RR = PT2/PT0 = F(Wc2, Mach,..)
  Civil turbofans : RR > 0.95
  Military

## Slide 49: Inlet flow distortion
Cross wind

## Slide 50: Inlet efficiency (2)
Engineering practice
  no isentropic efficiency
Instead represent losses using
  RR Ram recovery factor = Pt2/Pt0 ~ 0.6? - 0.97
  F16 Inlet RR = ~ 0.98 @ cruise
  F16 Inlet RR = ~ 0.89 @ MIL Take-off V=0 !

## Slide 51: Jet engine exhaust nozzle
expansion (conversion of Epot (pressure) to Ekin)
subsonic & supersonic
geometry
losses
shock waves
cold (turbofan) versus hot exhaust
mixed flow
thrust reversing

## Slide 52: Exhaust nozzles
Small pressure loss
Wc
PR (Ptin / Po)
Choking Ma> = 1 PR ~ 1.9

## Slide 53: Nozzle efficiency (3)
Engineering practice
  no isentropic efficiency
Instead represent losses using
  CD discharge coefficient = Aeff/Ageom ~ 0.95-0.97
  CV velocity coefficient = Cj/Cjdeal ~ 0.95-0.98
  CX thrust coefficient = FG/FGideal ~ 0.95-0.98
  CV ~ CX represent similar loss

## Slide 54: Critical pressure ratio
amb
p
omg
p
res
m
p
res
/p
omg
p
res
= konst
g
kr
p
amb
= konst
cr
amb
amb
const
const

## Slide 55: Isentropic expansion

## Slide 56: Nozzle area and Mach number


throat

## Slide 57: Non-isentropic expansion
M=1

## Slide 58: Gas turbine system performance
Component characteristics
  intake, fans/compressors
  combustion chambers, turbines, mixers, exhausts
  limits (stall, rotational speeds, temperatures....)
Engine Characteristics
  gas turbine system: Rotor speeds, FN, PW, TRQ, WF, SFC, etc.
  steady-state vs. transient
Power Limitations
  limits: temperature, pressure, rotor speeds, stall, ....

## Slide 59: Complete expansion
  Calculation recipe for unchoked nozzle (complete expansion to p0 at nozzle throat or nozzle exit)

## Slide 60: Incomplete expansion
  Calculation recipe for choked nozzle (incomplete expansion to pj at nozzle throat, residual expansion beyond throat)
solve for ceff

## Slide 61: Converging vs. Converging-diverging
“Convergent vs. ‘Con-Di’ nozzle”
Difference in design thrust
Nozzle pressure ratio
  Application (e.g., F-16)
Off-design performance
Relation thrust  drag
Weight, length, etc.

## Slide 62: TJET turbine performance in GSP

## Slide 63: Other components performance characteristics
Ducts
  Pressure loss function of flow (Wc) or Mach or other
Inlets
  Simular to ducts
  Also function of flight conditions (Maflight )
Heat loss effects
  All components
  Heat transfer models
Other components
  Specific effects on gas path

## Slide 64: Gas turbine (‘whole engine’) characteristics
p
0,2
p
m
 T
N
 T
0,2
p
0,3
0,2
0,2
T
0,2
T
0,4
Equilibrium running lines in component characteristics

## Slide 65: Recuperation
Transfer exhaust heat to preheat combustor flow
  Saving fuel
Adds substantial mass and volume to the gas turbine system
Expensive
  Tough recuperator heat exchanger design requirements
  High manufacturing costs
Aero engine application
  Topic of research
  So far, high mass and volume too high
  Additional reliability and safety issues

## Slide 66: Power limitation
“Flat rating” = FN, Power/TRQ limitation at low T0,2
N
2
T
0,3
p
2
(max. internal pressure)
(HD-shaft)
Shaft power or Thrust
-40
-30
-20
-10
0
10
20
30
40
Ambient temperature sea level
ISA

## Slide 67: Performance limitations
limits: temperature, pressure, rotational speed, stall, ....
steady-state
  variation T0 
  variation P0
acceleration
deceleration
control
p
0,2
p
m
 T
N
 T
0,2
p
0,3
0,2
0,2
T
0,2
T
0,4
equilibrium running line
O
A
B

## Slide 68: AE4263 Modeling, Simulation and Application of Power and Propulsion Systems
Lectures + work shop 2nd semester 3+2 ECTS
Performance prediction of gas turbine engines
  aero engines (AE)
  industrial engines (3mE)
Understand/analyze engine behaviour
  Design point and off-design
Gas turbine Simulation Program GSP (www.gspteam.com)
https://online-learning.tudelft.nl/courses/modeling-simulation-and-application-of-power-and-propulsion-systems/
https://brightspace.tudelft.nl/d2l/home/45948