## Slide 1: Build your own gas turbine performance model in Python
Tutorial of Basics
ASME IGTI TE 2025 Aircraft Engine Committee
Dr. Wilfried Visser
Oscar Kogenhop MSc

## Slide 2: Overview
Introduction
System performance modelling
Gas turbine performance system models
Software implementation aspects
Case study: jet engine python model
Concluding remarks

## Slide 3: Introduction
Aircraft propulsion system performance prediction
  Design studies
  Existing engines
New elements
  Sustainable fuels
  Electric systems
  Heat exchangers
  Hybrid systems (gas turbines, fuel cells, batteries)
  Generators
  Electric motors driving fans and propellers
Need for
  Extensions in modeling and simulation tools ?
  Built tools from scratch ?

## Slide 4: System performance modeling
System of interacting components
Component models
Relationships among components
Equations (mostly non-linear differential)
  conservation of mass, energy, momentum, …
Component operating points
  Defined by state variables
Solution of set of equations
  State variable vector representing valid system operating point
  Steady-state or transient

## Slide 5: Software implementation issues
So you have decided to start from scratch!
Things to think about
  Will others use my code?
  Will code be used later?
    For other propulsion systems / engines?
  Costs / Benefits of making the tool generic?
    Add a user friendly GUI?
  Flexibility
  ….?...
Save time and $ preparing your project
  Language, development platform
  Software architecture

## Slide 6: Language / development environment
Python
  Open source
  Widely used by students, young engineers and scientists
  Ready to use libraries for almost any engineering problem
  Object orientation
  Readable code
Development environments
  Microsoft Visual Studio Code (‘VS Code’)
  PyCharm
Platform? Windows, Linux, IOS?

## Slide 7: Python implementation - numerics
Run from code (no GUI)
  Specify input in code
  Adapt code where needed
Ready to use libraries
  Standard atmosphere aero-calc
  Thermodynamics cantera
    Compression, expansion in compressors, turbine, exhausts, nozzles
    Combustion chemical reactor model
  Numerical methods scipy
    ‘root’ generic solver (‘Krylov’ method)
  Output data export
    Export to .csv pandas
    Make graphs in Excel

## Slide 8: Python implementation - output
Generate global output table pandas
  Code output per component
  System level output (PW, FN, Wf, W2 etc.)
  Export to .csv
  Make graphs in Excel
Component maps
  Graphical output matplotlib
  Compessors, fans, turbines, …
  Draw operating lines in maps
    scaling

## Slide 9: Adapting the baseline code
Other fuels
  Easily adapt fuel in combustor component (cantera)
Other engine configurations
  Turbofan
  Turbogenerator
Add propulsion system elements
  Generators, electric motors, propulsors, batteries, fuel cells
Extend output
Add GUI ?

## Slide 10: Object orientation
3 main paradigms
  Encapsulation
    An object holds both data and ‘methods’ (procedures, functions) working with these and data, and also external data
    Object class (class is ‘type’ of object)
  Inheritance
    An object can inherit data and methods from a ‘parent class’
  Polymorphism
    An object variable can represent objects from different classes inheriting from the same parent

## Slide 11: Polymorphism
Abstract Generic component model class
  Encapsulation
    An object holds both data and ‘methods’ (procedures, functions) working with these and data, and also external data
    Object class (class is ‘type’ of object)
  Inheritance
    An object can inherit data and methods from a ‘parent class’
  Polymorphism
    An object variable can represent objects from different classes inheriting from the same parent

## Slide 12: Encapsulation example
Compressor component model
  “compressor” object class holds
    W, PR, Eta, N
    methods to calculate the compression process
    Functions to communicate with the system model and other component models

## Slide 13: Inheritance example
Gas path W, T, P in/out
Inlet
Turbomachinery N, PR, Eta, PW
Controls
Fuel control
Duct
Combustor fuel flow
….
Compressor compression
Turbine expansion
Fan splitter
….
Exhaust PR, thrust
instantiable class
abstract class
Generic component model class
data
functions, procedures (algorithms)
legend

## Slide 14: Polymorphism example
“Generic component model” class object
  ‘abstract’ object that can represent any child object
  has a generic ‘Run’ method (procedure or function)
  Child classes inherit and ‘override’ the Run procedure with calculations actually simulating the process in the component
System model
  List of objects (of instantiable classes)
    E.g. Inlet-compressor-combustor-turbine-exhaust
    System model simulation subsequently calls the ‘Run’ methods of all objects in the list, in this example calculating from inlet through exhaust….
Abstract Generic component model class
  Encapsulation
    An object holds both data and ‘methods’ (procedures, functions) working with these and data, and also external data
    Object class (class is ‘type’ of object)
  Inheritance
    An object can inherit data and methods from a ‘parent class’
  Polymorphism
    An object variable can represent objects from different classes inheriting from the same parent

## Slide 15: Polymorphism python code example
# create a turbojet model list of component models
turbojet = [TInlet( 'Inlet1', 19.9, 1 ),
TCompressor('compressor1', 1, 16540, 6.92, 0.825),
TCombustor( 'combustor1', 0.38, 0, 1, 1 ),
TTurbine( 'turbine1', 1, 16540, 0.88 ),
TDuct( 'exhaustduct', 1 ),
TExhaust( 'exhaust1', 1, 1, 1 )]
……
# comp is the abstract component object
for comp in turbojet:
q_gas = comp.Run(Mode, q_gas, Ambient)
Class
Name
Class data

## Slide 17: Extending the models - 1
Fidelity
  1-D component models
    Turbomachinery
    Combustors
  Couple with multi-D CFD models
Gas turbine system
  Control system
  Fans, mixers
  Recuperators

## Slide 18: Extending the models - 2
Propulsion system elements
  Loads (propellers, generators)
  Hybrid propulsion systems
    Batteries
    Fuel cells

## Slide 19: Gas turbine performance
Component Characteristics
  intake, fans/compressors
  combustion chambers, turbines, mixers, exhausts
  limits (stall, rotational speeds, temperatures....)
Engine Characteristics
  gas turbine system: Rotor speeds, FN, PW, TRQ, WF, SFC, etc.
  steady-state vs. transient
Power Limitations
  limits: temperature, pressure, rotor speeds, stall, ....

## Slide 20: T-S diagram, turbojet IDEAL cycle
T
S
0
2
3
c02
2cp
C0 = air speed
C8 = propelling jet velocity
4
5
8
turbine
nozzle
c82
2cp
p0
inlet ram compression

## Slide 21: Aero engine inlet ram compression
Jet engine inlet example
internal diffusion (compression)
external diffusion (compression)
“inlet efficiency”
0
1
2

## Slide 22: T-S diagram, turbojet REAL cycle
T
S
0
2
3
c02
2cp
C0 = air speed
C8 = propelling jet velocity
4
5
8
turbine
nozzle
c82
2cp
1
pressure loss
station 1 = inlet front
1-2 : inlet losses
p0

## Slide 23: T-S diagram, afterburning turbojet (reheat)
T
S
c02
2cp
C0 = air speed
C8 = propelling jet velocity
0
2
3
4
5
8 (9 with con-di nozzle)
turbine
nozzle
c82
2cp
1
pressure loss
p0
afterburner

## Slide 24: T-S diagram, turbofan REAL cycle
T
S
0
2
3
c02
2cp
unmixed turbofan
C0 = air speed
C8 = propelling jet velocity
4
5
8
HP turbine
hot nozzle expansion
c82
2cp
1
pressure loss
cold nozzle expansion
25
p0
45
LP turbine

## Slide 25: Dimensionless groups
Turbomachinery
  Compressors, Fans, Turbines
  (propellers, helicopter rotors)
Performance representation (ideal gas)
  ‘Function’ of D, N, m, P01, P02, T01, T02, ν (or μ), γ (cp/cv)
  Dimensional analysis (Pi theorem):
    3 fundamental units present (M, T, L)
    Number of variables reducible by 3 into 9-3 = 6 non-dim. groups
    Relations among which describe performance
  4 primary groups
  2 groups often ignored for gas turbines
    effect viscosity ν or μ (Re) marginal on efficiency, ‘only’ high altitude
    Gamma γ only if using different media (e.g. process industry, organic rankine, scCO2 cycles) or large temperature changes (γ = F(T))
D
m
N
γ, μ
P02, T02
P01, T01

## Slide 26: Dimensionless groups - Reynolds
Effect of kinematic viscosity ν represented by Reynolds number
For axial turbomachinery:
  (L = blade chord length, V is blade relative velocity, ν = kinematic viscosity)
Effect of Re is small
  Primarily on efficiency
    Small corrections as function of Re change
  Aero engines
    at high altitudes / low ambient temperatures
    higher ν (= μ/ρ)

## Slide 27: Compressor characteristics
Equilibrium running line
h
p
m
θ
N
θ
A
0,2
p
0,3
comp
Surge line
curves of constant
δ

## Slide 28: Turbine characteristics
N
θ
N
θ
PR =p
/
p
h
m
θ
δ
choking
turb
0,4
0,5

## Slide 29: Inlet characteristics
Pressure loss function
  ‘Ram recovery’ RR = PT2/PT0 = F(Wc2, Mach,..)
  Civil turbofans : RR > 0.95
  Military

## Slide 30: Inlet flow distortion
Cross wind

## Slide 31: Inlet efficiency (2)
Engineering practice
  no isentropic efficiency
Instead represent losses using
  RR Ram recovery factor = Pt2/Pt0 ~ 0.6? - 0.97
  F16 Inlet RR = ~ 0.98 @ cruise
  F16 Inlet RR = ~ 0.89 @ MIL Take-off V=0 !

## Slide 32: Jet engine exhaust nozzle
expansion (conversion of Epot (pressure) to Ekin)
subsonic & supersonic
geometry
losses
shock waves
cold (turbofan) versus hot exhaust
mixed flow
thrust reversing

## Slide 33: Exhaust nozzles
Small pressure loss
Wc
PR (Ptin / Po)
Choking Ma> = 1 PR ~ 1.9

## Slide 34: Nozzle efficiency (3)
Engineering practice
  no isentropic efficiency
Instead represent losses using
  CD discharge coefficient = Aeff/Ageom ~ 0.95-0.97
  CV velocity coefficient = Cj/Cjdeal ~ 0.95-0.98
  CX thrust coefficient = FG/FGideal ~ 0.95-0.98
  CV ~ CX represent similar loss

## Slide 35: Critical pressure ratio
amb
p
omg
p
res
m
p
res
/p
omg
p
res
= konst
g
kr
p
amb
= konst
cr
amb
amb
const
const

## Slide 36: Isentropic expansion

## Slide 37: Nozzle area and Mach number


throat

## Slide 38: Non-isentropic expansion
M=1

## Slide 39: Complete expansion
  Calculation recipe for unchoked nozzle (complete expansion to p0 at nozzle throat or nozzle exit)

## Slide 40: Incomplete expansion
  Calculation recipe for choked nozzle (incomplete expansion to pj at nozzle throat, residual expansion beyond throat)
solve for ceff

## Slide 41: Converging vs. Converging-diverging
“Convergent vs. ‘Con-Di’ nozzle”
Difference in design thrust
Nozzle pressure ratio
  Application (e.g., F-16)
Off-design performance
Relation thrust  drag
Weight, length, etc.

## Slide 42: TJET turbine performance in GSP

## Slide 43: Compressor stall
direction of rotation
rotor blade
air flow
u
cabs
crel

rotor blade leading edge velocity triangle
excessive blade incidence angle α causes boundary layer break-down
stator vane

## Slide 44: Rotating stall
B
C
A
direction of rotation
direction of stall
rotational direction rotor
Rotational
direction stall cell
stall cell
stall cell
stall cell
part span
full span
full span

## Slide 45: Stall at low rotor speeds
p
0,2
Equilibrium running line
p
m
T
N
T
1
0,2
p
0,3
Surge line
01
01
2
3
T0,2
T0,2

## Slide 46: Stall at low rotor speeds (2)
c
a.1
c
a.1
w
1
w
2
u
c
1
c
2
U
1
u
2
=
3
c
a.2
c
a.3b
c
a.3a
final stages
first stages
a.
b.

## Slide 47: Enhancing operability at low speeds
direction of rotation
rotor blade
u
cabs
crel

Compressor
front stage velocity triangles
stator vane
low speed stall
Design point speed

## Slide 48: Enhancing operability at low speeds
direction of rotation
rotor blade
u
cabs
crel

Compressor
front stage velocity triangles
stator vane
low speed stall
Design point speed
variable bleed valves
Variable bleed/blow-off valves (vbv’s)
  usually start-up only

## Slide 49: Enhancing operability at low speeds
direction of rotation
rotor blade
u
cabs
crel

Compressor
front stage velocity triangles
stator vane
low speed stall
Design point speed
multi-spool
Multi-spool

## Slide 50: Enhancing operability at low speeds
direction of rotation
rotor blade
u
cabs
crel

Compressor
front stage velocity triangles
stator vane
low speed stall
Design point speed
variable geometry
Variable geometry (vigv’s and vsv’s)
design point vsv position
low speed vsv position
cabs

## Slide 51: Enhancing operability at low speeds
direction of rotation
rotor blade
u
cabs
crel

Compressor
front stage velocity triangles
stator vane
low speed stall
Design point speed
variable bleed valves
multi-spool
variable geometry
Variable bleed/blow-off valves (vbv’s)
  usually start-up only
Multi-spool
Variable geometry (vigv’s and vsv’s)
design point vsv position
low speed vsv position
cabs

## Slide 52
Variable stator vanes (VSV)
Courtesy: Rolls Royce ‘The Gas Turbine’
‘Variable inlet
guide vanes’ (VIGVs)
1st stage rotor blades
Compressor inlet flow

## Slide 53
Variable stator vanes (VSV)

## Slide 54
Variable Bleed Valve (VBV)
Courtesy: Rolls Royce ‘The Gas Turbine’

## Slide 55: Stall – operational considerations
Surge
  Pumping
  Radial compressors
  “extreme” form c.q. consequence of STALL
Pressure ratio
Mass flow
3
k
2
k
1
compressor
valve (3 positions)
A
1
2
k
3

## Slide 56: Stall initiation and recovery
‘surge’

## Slide 57: Other components performance characteristics
Ducts
  Pressure loss function of flow (Wc) or Mach or other
Inlets
  Simular to ducts
  Also function of flight conditions (Maflight )
Heat loss effects
  All components
  Heat transfer models
Other components
  Specific effects on gas path

## Slide 58: Gas turbine (‘whole engine’) characteristics
p
0,2
p
m
 T
N
 T
0,2
p
0,3
0,2
0,2
T
0,2
T
0,4
Equilibrium running lines in component characteristics

## Slide 59: Characteristics jet engine vs. turboshaft
p
0,2
p
m
 T
N
 T
0,2
p
0,3
0,2
0,2
T
0,2
T
0,4
Equilibrium running line
of a gas turbine with
free power turbine
or nozzle
Operating line of a single-shaft gas turbine
(const. speed drive, e.g. for electricity generation)

## Slide 60: Characteristics 2-shaft turboshaft (free PT)
2
1.5
1.2
1.05
sfc
sfc
o
PW
PWo
1
0
0
1
0.75
0.80
0.85
0.90
0.95
1.0
PT
o
N
PT
N
GG
GG
o
N
N

## Slide 61: Comparison TurboshaftDiesel engine
2
TRQ
o
TRQ
1
0
0
1
shft
o
N
shft
N
0,25
0,5
0,75
0,5
1,5
2 - shaft gas turbine
Diesel engine
1 - shaft gas turbine

## Slide 62: Part load performance
Gas turbines (simple cycle) generally suffer from poor part load efficiency
Options to mitigate this effect
  “flatten the SFC curve”
  Recuperation
  Variable geometry
Excellent topic to analyse using a system simulation tool like GSP

## Slide 63: NLR GSP www.nlr.nl/public/hosted-sites/gsp

## Slide 64: 2-spool turboshaft engine performance
Varying power turbine speed
Problem: high SFC at low NP rotational speed

## Slide 65: 2-spool turboshaft engine performance
Problem: high SFC at part-load
SFC at constant NPT , decreasing power and torque

## Slide 66: Recuperation
Transfer exhaust heat to preheat combustor flow
  Saving fuel
Adds substantial mass and volume to the gas turbine system
Expensive
  Tough recuperator heat exchanger design requirements
  High manufacturing costs
Aero engine application
  Topic of research
  So far, high mass and volume too high
  Additional reliability and safety issues

## Slide 67: Recuperated micro turbine test rig
From: Visser W.P.J., Shakariyants S.A. , Oostveen M. ‘Development of A 3kW Micro Turbine For CHP Applications’, ASME Journal of Engineering for Gas Turbines and Power, April 2011, Vol. 133 / 042301-1

## Slide 68: MTT Enertwin 3kW micro turbine
Recuperated micro turbine
Small scale Combined Heat Power (CHP)
Thermal efficiency ~ 18%
Visser W.P.J., Shakariyants S.A. , Oostveen M. ‘Development of A 3kW Micro Turbine For CHP Applications’, ASME Journal of Engineering for Gas Turbines and Power, April 2011, Vol. 133 / 042301-1

## Slide 69: Honeywell AGT1500C recuperated turboshaft

## Slide 70: Adapting component characteristics
surge line
A
B

m*
 T
p
Variable geometry
Fixed geometry
d
= 0
_
+
Stator
surge line
S
A
B
B'
0,2
0,2
A'
running line
Running lines
stator
closed
open
a
b
variable geometry
compressor:
  variable bleed valves (VBVs)
  variable stator vanes (VSVs)
  variable inlet guide vanes (VIGVs)
turbine:
  VSVs 
  improving SFC, TRQ at part-load

## Slide 71: Power limitation
“Flat rating” = FN, Power/TRQ limitation at low T0,2
N
2
T
0,3
p
2
(max. internal pressure)
(HD-shaft)
Shaft power or Thrust
-40
-30
-20
-10
0
10
20
30
40
Ambient temperature sea level
ISA

## Slide 72: Performance limitations
limits: temperature, pressure, rotational speed, stall, ....
steady-state
  variation T0 
  variation P0
acceleration
deceleration
control
p
0,2
p
m
 T
N
 T
0,2
p
0,3
0,2
0,2
T
0,2
T
0,4
equilibrium running line
O
A
B

## Slide 73
Jet engine performance
Power setting (Ngg) and flight condition
FN = W*(Cj-C0)
ρ ~ P0/T0
W ~ N*ρ
FF ~ W
Low Re
To drop

## Slide 74: Standard atmosphere profiles

## Slide 75: Volcanic ash and performance
Sandpapering (erosion)
Contamination with ‘molten glass’
  Blocking cooling holes
From BBC
  http://www.youtube.com/watch?v=3JtCewoqnzA&list=HL1323349650&feature=mh_lolz

## Slide 76: AE4263 Modeling, Simulation and Application of Power and Propulsion Systems
Lectures + work shop 2nd semester 3+2 ECTS
Performance prediction of gas turbine engines
  aero engines (AE)
  industrial engines (3mE)
Understand/analyze engine behaviour
  Design point and off-design
Gas turbine Simulation Program GSP (www.gspteam.com)
https://online-learning.tudelft.nl/courses/modeling-simulation-and-application-of-power-and-propulsion-systems/
https://brightspace.tudelft.nl/d2l/home/45948