## Slide 1: Build your own gas turbine performance model in Python
Tutorial of Basics
ASME IGTI TE 2025 Aircraft Engine Committee
Dr. Wilfried Visser
Oscar Kogenhop MSc

## Slide 2: Overview
Introduction
System performance modelling
  Propulsion and power systems
Software implementation
  Example case: jet engine python model
Concluding remarks

## Slide 3: For whom is this tutorial
Engineers, scientists, researchers, students
  With interest in system simulation of propulsion and power systems
  Wanting to learn how system models work
  Needing for models with new functionalities
    Coupling with other models
  Having basic coding skills
Introduction

## Slide 4: Key focus areas
System modelling
Object orientation
Python programming language
  Open-source libraries
    Aero-thermal
    Numerical methods
    Data handling
    Visualization
Introduction

## Slide 5: System performance modeling
System of interacting components
  Relationships among system of interacting components
  Component models
Equations
  conservation of mass, energy, momentum, other…
  mostly non-linear algebraic/differential
Component operating points
  Defined by state variables
Solution of set of equations
  State variable vector representing valid system operating point
  Steady-state or transient

## Slide 6: Propulsion and power systems
Gas turbines
  Aero engines: jet engines, turboprop, turboshaft
  Land based engines: turboshaft
Propellers and rotors
Hybrid elements
  Electric motors
  Generators
  Fuel cells
  Batteries
Alternative/sustainable fuels
System performance modeling

## Slide 7: Propulsion and power system performance prediction
Design studies
Existing designs
System performance modeling

## Slide 8: Gas turbine system performance models
Components models
  intake, fans/compressors, combustors, turbines, mixers, exhausts,
  Component maps
State variables
  Rotor speeds, mass flows, pressure ratios, …
Equations
  Mass flow in = mass flow out (at component intersections, engine stations)
  Power balance : PWcompressor = PWturbine
Input
  Fuel flow, TIT, inlet P and T…
Output
  Thrust FN, Power, Fuel flow, Efficiency, P, T at engine stations…
System performance modeling

## Slide 9: Relationships among component models
Ambient
  Inlet, exhausts
Gas path
  Gas conditions and flow rates between two connected components
  Engine station numbering
  Example: compressor – combustor, station nr. 3
Shafts
  Power balance PWcompressor = PWturbine
  If no balance: transient (accel or decel)
Heat transfer
Control
  Fuel flow, variable geometry
Software implementation

## Slide 10: Design point simulation
Design studies
Effects of cycle design parameters
  e.g. PR, BPR, W, efficiencies
Varying dimensions
Simple
  straight forward inlet to exhaust calculation
  conservation of mass, energy, momentum
More complex
  solving equations
  constraints
System performance modeling

## Slide 11: Design point calculation example
Single spool Turbojet
Gas turbine performance models
Start DP calculation through CalcList
Pt2, Tt2, FD
P0, T0, Ma, W2des
Combustor
Output
Input
PRcdes
ηcdes
Wfdes
ηtdes
Exhaust nozzle
8
5
Turbine
4
Manual Fuel Control
3
Compressor
2
End of simulation
Pt3, Tt3, W3
Pt4, Tt4, W4
Pt5, Tt5, W5
Ps8, Ts8,
A8, FG
Post processing
FN, SFC
Initialization:
Check model consistency
Build ordered component list CalcList
Inlet
0

## Slide 12: Off-design (‘OD’) simulation
Analyze effects of operating conditions on performance
Fixed geometry and dimensions
  *except for variable geometry features like VSVs, IGVs, Bleed valves
Requires initially calculated Design point
  ‘cycle reference point’ CRP
Predict how the operating point changes (from CRP) with operating conditions deviating from the design conditions
  Steady-state equilibrium
  Transient (change in time, accel/decel of rpm’s)
System performance modeling

## Slide 13: Equations and numerical methods
Solve equations for a gas turbine engine steady-state or transient OD operating point
State variables
  representing the operating point
  minimal number of independent (or ‘tearing’) variables
  other parameters can be directly/explicitly calculated from the state variable values
Find the OD operating point = find state variable values
  Satisfying all conservation equations
  Residuals (‘errors’) must all be 0
Single solution
  n ‘error equations’ with n unknown ‘state variables’ (n degrees of freedom system)
  Calculate all dependent other parameter values
System performance modeling

## Slide 14: Turbojet example - states
Required: 4 states S1..4
  S1 = W2
  S2 = PRc*
  S3 = N
  S4 = PRt
From the 4 states all other parameters can be calculated
*Instead of PR, usually Beta is used
Off-design simulation
2
3
4
5
C
T
0
8
0
W2
PRc
N
PRt

## Slide 15: Turbojet example - equations
Satisfying conservation equations
To find the 4 unknown states we need 4 equations
  E1 = Inlet mass flow - compressor mass flow (map) = 0
  E2 = Compressor power + turbine power = 0
  E3 = Combustor exit mass flow - turbine mass flow (map) = 0
  E4 = Turbine mass flow - nozzle mass flow = 0
Off-design simulation
2
3
4
5
C
T
0
8
0
E1
E4
E2
E3
P5
T5

## Slide 16: Off-design iteration flow chart - turbojet
Gas turbine performance models
Start OD calculation through CalcList
S[1]→Wc2
Combustor
Input
S[2]→N
S[3]→βc
Wf OD
S[2]→N
S[4]→βt
Exhaust nozzle
8
5
Turbine + map
4
Manual Fuel Control
3
Compressor
2
End of simulation
Post processing
OD performance
FN, SFC etc.
Initialize: set map scale factors,
assign State variables (S) and Error functions (E), determine first J-1
Define States And Errors
Inlet
0
y
n
P0, T0, Ma
n
Not enough progress
determine new J-1
y

## Slide 17: Recommended literature
W. Visser “Generic Analysis Methods for Gas Turbine Engine Performance: the development of the gas turbine simulation program GSP”, 6 January 2015, Delft University of Technology, ISBN 978-94-6259-492-0 (available from https://repository.tudelft.nl/islandora/object/uuid%3Af95da308-e7ef-47de-abf2-aedbfa30cf63 ).
H. I. H. Saravanamuttoo, G. F. C. Rogers and H. Cohen, Gas Turbine Theory, 5th ed.: Pearson Education, 2001.
Several authors and contributors, ‘AVT-018 Performance Prediction and Simulation of Gas Turbine Engine Operation’, NATO Research and Technology Organization 2003 RTO-TR-044
Walsh P.P, Fletcher P., Gas turbine Performance, ISBN-10: ‎ 063206434X ISBN-13 ‏ : ‎ 978-0632064342
Visser, W.P.J. and Broomhead M.J., 2000, ‘GSP, a generic object-oriented gas turbine simulation environment’, ASME paper 2000-GT-2, presented at the ASME TURBO EXPO 2000, 8-11 May 2000, Munich, Germany,
J. Kurzke, "Advanced User-friendly Gas Turbine Performance Calculations on a Personal Computer", 95-GT-147, presented at the ASME IGTI Turbo Expo, 1995.`
J. Kurzke, "How to get Component Maps for Aircraft Gas Turbine Performance Calculations", ASME Paper 96-GT-164, 1996.
W. P. J. Visser and I. D. Dountchev, "Modeling Thermal Effects on Performance of small Gas Turbines", GT2015-42744, to be presented at the ASME IGTI Turbo Expo 2015, Montreal, Canada, 2015.

## Slide 18: New propulsion system model elements
Sustainable fuels
Electric systems
Heat exchangers
Hybrid systems (gas turbines, fuel cells, batteries)
Generators, Electric motors driving fans and propellers
So, there is a need for
  Extensions in modeling and simulation tools
  Or, build tools from scratch ?
System performance modeling

## Slide 19: From scratch ?
Things to think about
  Why from scratch?
  Will others use my code?
  Will code be used later?
    For other propulsion systems / engines?
    Flexibility
  Costs / Benefits of making the tool generic?
    Add a user-friendly GUI?
  ?...
Save time and $ preparing your project
  Select language, development platform
  Design software architecture
System performance modeling

## Slide 20: Why from scratch?
Pros
  Full control and flexibility
  “I know what I am doing”
  Coupling with other models (1..4 D models)
Cons
  A lot of work
    Validation
    Code maintenance / documentation
  Code accessibility / readability to others
    Especially ‘if you leave the company’
System performance modeling

## Slide 21: Software implementation
So, you have decided to start
from scratch!

## Slide 22: Language / development environment
Python
  Open-source programming language/development environment
  Widely used by students, young engineers and scientists
  Ready to use libraries for almost any engineering problem
  Object orientation
  Readable code
Development environments
  Microsoft Visual Studio Code (‘VS Code’)
  PyCharm
Platform? Windows, Linux, IOS?
Software implementation

## Slide 23: Python versus previous experience
Gas turbine Simulation Program GSP
  Developed at
    Dutch National Aerospace Center NLR
    Delft University of Technology
  Object oriented, GUI
  4GL development environment, 30 year legacy code
  ~120,000 lines of code (excluding library code)
Python “GSPy”
  using open-source libraries
  ~ 1000 - 4000 lines of code !!!!
Software implementation

## Slide 24: Working with Python models
Run code from development environment (no GUI)
Specify input in code
  Example: specify Ambient conditions and a number of fuel flow steps
Adapt / extend code where needed
Software implementation

## Slide 25: Python models overview
Object oriented architecture
Main program
Using open-source libraries
Component model implementations
Output of simulation results
Software implementation

## Slide 26: Object orientation
3 main paradigms
  Encapsulation
    An object holds both data and ‘methods’ (procedures, functions) working with these and data, and also external data
    Object class (class is ‘type’ of object)
  Inheritance
    An object can inherit data and methods from a ‘parent class’
  Polymorphism
    An object variable can represent objects from different classes inheriting from the same parent
Software implementation

## Slide 27: Encapsulation example
Compressor component model
  compressor object class holds
    W, PR, Eta, N
    methods to calculate the compression process
    Compressor performance map
    Functions to communicate with the system model and other component models
Object orientation

## Slide 28: Inheritance example
Gas path W, T, P in/out
Inlet
Turbomachinery N, PR, Eta, PW
Controls
Fuel control
Duct
Combustor fuel flow
….
Compressor compression
Turbine expansion
Fan splitter
….
Exhaust PR, thrust
instantiable class
abstract class
Generic component model class
data
functions, procedures (algorithms)
Object orientation
legend

## Slide 29: Polymorphism example
Generic component model class object
  ‘abstract’ object that can represent any child object
  has a generic ‘Run’ method (procedure or function)
  Child classes inherit and ‘override’ the Run procedure with calculations actually simulating the process in the component
System model
  List of objects (of instantiable classes)
    E.g. Inlet-compressor-combustor-turbine-exhaust
    System model simulation subsequently calls the ‘Run’ methods of all objects in the list, in this example calculating from inlet through exhaust….
Abstract Generic component model class
  Encapsulation
    An object holds both data and ‘methods’ (procedures, functions) working with these and data, and also external data
    Object class (class is ‘type’ of object)
  Inheritance
    An object can inherit data and methods from a ‘parent class’
  Polymorphism
    An object variable can represent objects from different classes inheriting from the same parent
Object orientation

## Slide 30: Polymorphism python code example
# create a turbojet model list of component models
turbojet = [TInlet( 'Inlet1', 19.9, 1 ),
TCompressor('compressor1', 1, 16540, 6.92, 0.825),
TCombustor( 'combustor1', 0.38, 0, 1, 1 ),
TTurbine( 'turbine1', 1, 16540, 0.88 ),
TDuct( 'exhaustduct', 1 ),
TExhaust( 'exhaust1', 1, 1, 1 )]
……
# comp is the abstract component object
for comp in turbojet:
q_gas = comp.Run(Mode, q_gas, Ambient)
Object orientation
Class
Name
Design/object data

## Slide 31: Main program for turbojet DP & OD simulation
Software implementation
(key code lines only)
Create Oper.conds.
Model creation &
definition
Procedure running
all comps.
DP simulation
OD simulation using root to
Find OD points

## Slide 32: Main program code
# Generic gas turbine components
inlet1 = TInlet('Inlet1', '', 0,2, 19.9, 1 )
duct1 = TDuct('exhduct', '', 5,7, 1.0 )
exhaust1 = TExhaust('exhaust1', '', 7,8,9, 1, 1, 1, 1 )
# ***************** Combustor ******************************************************
# fuel input
combustor1 = TCombustor('combustor1', '', 3, 4, 0.38, None, 1, 1, None, 43031, 1.9167, 0, '')
compressor1 = TCompressor('compressor1','compmap.map' , 2, 3, 1, 16540, 0.825, 1, 0.75 , 6.92, 'GG')
turbine1 = TTurbine( 'turbine1' ,'turbimap.map', 4, 5, 1, 16540, 0.88 , 1, 0.50943, 0.99, 'GG’)
fsys.systemmodel = [inlet1,
compressor1,
combustor1,
turbine1,
duct1,
exhaust1]
Software implementation

## Slide 33: Example: define a turbojet model
# Generic gas turbine components
inlet1 = TInlet('Inlet1', '', 0,2, 19.9, 1 )
duct1 = TDuct('exhduct', '', 5,7, 1.0 )
exhaust1 = TExhaust('exhaust1', '', 7,8,9, 1, 1, 1, 1 )
# ***************** Combustor ******************************************************
# fuel input
combustor1 = TCombustor('combustor1', '', 3, 4, 0.38, None, 1, 1, None, 43031, 1.9167, 0, '')
compressor1 = TCompressor('compressor1','compmap.map' , 2, 3, 1, 16540, 0.825, 1, 0.75 , 6.92, 'GG')
turbine1 = TTurbine( 'turbine1' ,'turbimap.map', 4, 5, 1, 16540, 0.88 , 1, 0.50943, 0.99, 'GG’)
fsys.systemmodel = [inlet1,
compressor1,
combustor1,
turbine1,
duct1,
exhaust1]
Software implementation

## Slide 34: Passing gas conditions in Python
# use dictionary for gas path conditions oriented by gas path station number
gaspath_conditions = {}
def Run(self, Mode, PointTime):
…
self.GasIn = fsys.gaspath_conditions[self.stationin]
…
# Calculate self.GasOut
…
fsys.gaspath_conditions[self.stationout] = self.GasOut
return self.GasOut
Software implementation

## Slide 35: Python open-source libraries
Ready to use libraries
  Standard atmosphere aero-calc
  Thermodynamics cantera
    Compression, expansion in compressors, turbine, exhausts, nozzles
    Combustion chemical reactor model
  Multidimensional arrays numpy
  Numerical methods scipy
    ‘root’ generic solver (‘Krylov’ method)
  Output data export
    Export to .csv pandas
    Make graphs in Excel
Software implementation

## Slide 36: Aero-calc library
Aero-calc functions used for calculation of ambient/flight conditions from altitude, flight Mach, dT
  alt2temp
  alt2press
  temp2speed_of_sound
Software implementation

## Slide 37: Cantera library
Open-source suite of tools for problems involving chemical kinetics, thermodynamics, and transport processes
https://cantera.org/index.html
Jetsurf machanism used for
  Gas path transport
  Compression/expansion
  Combustion
Software implementation
https://web.stanford.edu/group/haiwanglab/JetSurF/JetSurF2.0/Index.html

## Slide 38: Using Cantera (ct) gas model
  define gas model
    gas = ct.Solution('jetsurf.yaml’)
  Set T, P, composition (mass mixing ratios)
    gas.TPY = 1200, 101325, 'CH4:1, O2:2, N2:7.52’
  Get T or P
    P = gas.P
    T = gas.T
Software implementation

## Slide 39: Using Cantera (ct) mass flow/transport
  Define a quantity (mass flow) of gas
    GasIn = ct.Quantity(gas, mass flow)
  Set mass flow entropy or enthalpy and pressure
    GasIn.SP = entropy value, pressure value
    GasIn.HP = enthalpy value, pressure value
  Isentropic compression of GasIn mass flow (with pressure ratio PR)
Software implementation

## Slide 40: Using Cantera (ct) combustion
  2 options for fuel specification
    User specified composition (single species)
    T and P
  or
    User specified LHV (mix of ‘unknown’ species, e.g. Kerosine, Jet-A)
    T and P
    average H/C and O/C ratio of the fuel molecules
  In both cases end H, T, P and composition can be calculated
Software implementation

## Slide 41: User specified fuel composition
    fuel = ct.Quantity(fg.gas) define fuel
    fuel.mass = fuel mass flow fuel.TPY = T, P, FuelComposition define T, P, composition
    GasOut = GasIn + fuel mix fuel with air
    GasOut.equilibrate('HP’) chemical equilibrium combustion end state
    T4 = GasOut.T get combustion end T (or H, S etc)
Cantera - combustion

## Slide 42: User specified LHV
  More complicated
  Cannot use Equilibrate function
  Need to calculate end composition from
    Air composition
    Fuel H/C and O/C ratios
    Mole fractions book keeping (converting between mass – moles)
Cantera - combustion

## Slide 43: User specified LHV code
    Little bit more code lines:
Cantera - combustion

## Slide 44: Numpy and Scipy
https://docs.scipy.org/doc/
Numpy
  multidimensional array operations
Scipy
  solving system model non-linear algebraic/differential equations
  using Root function
    finding root of a vector function
      > a valid system steady-state or transient point
    newton-Raphson like iteration
    several solver methods
  Most suitable solver method ‘Krylov’
Software implementation

## Slide 45: Solver code
  Do_Run runs all component model code and returns the vector of equation errors (residuals)
  residuals is the vector function (returns all 0’s if states is valid OP)
  fsys.states = the initial value of the state vector
  solution = the state vector representing a valid operating point
Software implementation

## Slide 46: Component model implementations
Implementation of component performance maps
Inlets
Turbo machinery
  Compressors
  Fans
  Combustors
  Turbines
Ducts
Exhaust nozzles and diffusers
Software implementation

## Slide 47: Inlets
Component model implementations

## Slide 48: Compressors

## Slide 49: Python implementation - output
Generate global output table pandas
  Code output per component
  System level output (PW, FN, Wf, W2 etc.)
  Export to .csv
  Make graphs in Excel
Component maps
  Graphical output matplotlib
  Compessors, fans, turbines, …
  Draw operating lines in maps
    scaling
Software implementation

## Slide 50: Demonstration
Running single spool turbojet model
Environment Microsoft VScode
  Design + Off-design to IDLE at ISA SL
2 spool Turbofan

## Slide 51: Adapting the baseline code
Other engine configurations
  Turbofan
  Mixer
  Recuperator / heat exchanger
  Turbogenerator
Add propulsion system elements
  Generators, electric motors, propulsors, batteries, fuel cells
Software implementation

## Slide 52: Adapting the baseline code
Component model extensions
  Variable geometry
  Bleed
  Turbine cooling
  1-D model code
  Other fuels
    Easily adapt fuel in combustor component (cantera)
  …
Software implementation

## Slide 53: Adapting the baseline code
API (Application Programming Interface)
  Couple with other models
Extend user interface
  Extend output
    Graphs, tables, export
  Add GUI
Software implementation

## Slide 54: Extending the models - 1
Fidelity
  1-D component models
    Turbomachinery
    Combustors
  Couple with multi-D CFD models
Gas turbine system
  Control system
  Fans, mixers
  Recuperators
Application Programmers Interface API
Software implementation

## Slide 55: Extending the models - 2
Propulsion system elements
  Loads (propellers, generators)
  Hybrid propulsion systems
    Batteries
    Fuel cells
Software implementation

## Slide 56: Conclusion

## Slide 57: Questions?

## Slide 58: Other components performance characteristics
Ducts
  Pressure loss function of flow (Wc) or Mach or other
Inlets
  Simular to ducts
  Also function of flight conditions (Maflight )
Heat loss effects
  All components
  Heat transfer models
Other components
  Specific effects on gas path